## Slide 1: Presentation 4 – Better Practices for Water and Energy
Presented by
Chase Weinholtz
Derek Frommel
Gabriela Simoes
Guilherme Barbosa
1

## Slide 2: Better Practices for Water Sustainability
2

## Slide 3
Classifications of Used Water
There are generally a few classifications of water that undergoes treatment.
1. Blackwater – Comes from the Toilet, also called Sewage
2. Greywater – Comes from commercial buildings and households; usually water used for cleaning, cooking, etc.
          Dark Greywater – A subcategory of Greywater which contains heavy pollutants, usually from the sink or dishwasher.
3

## Slide 4: Desalination

## Slide 5
7
Why Desalination?
Desalination is a group of processes to remove salt and minerals from sea water or polluted water in order to obtain potable drinking water.
Used around the world in regions that lack access to clean water.

## Slide 6
Primary Methods of Desalination
Multi-Stage Flash (MSF) -- 13.5-25.5 kWh/m3
      Makes up more than half the world’s desalination
      Involves vaporizing water directly into steam.
      A condensate collector stores the pure water vapor
Multiple-Effect Distillation -- 6.5-11 kWh/m3
      Similar to MSF except the process takes place in tubes rather than tanks.
      This process uses thermal energy for heat transfer that can be reused.

## Slide 7
3. Vapor-Compression -- 7-12 kWh/m3
      This process involves evaporating and distilling seawater through a vapor compression refrigeration cycle
      The compressed vapor is condensed to pure liquid.
4. Reverse Osmosis -- 3-5.5 kWh/m3
      Involves filtering water through membrane pores (ranging from 0.1 to 5000 nm).
      These membranes can intercept bacteria, protozoa, and other microorganisms.
      Very energy efficient `
2
Primary Methods of Desalination

## Slide 8: Desalination Process
8
Notes: http://www.mercurynews.com/science/ci_25859513/nations-largest-ocean-desalination-plant-goes-up-near
http://www.amtaorg.com/water-desalination-processes
http://www.sswm.info/content/desalination

## Slide 9: Desalination – On a Large Scale
6
Chart: Israeli Water Desalination Facilities
| Ashkelon | Palmachim | Hadera | Sorek
 | 120 | 45 | 127 | 228
Total Output
520 million m3/year or roughly 420,000 acre ft./year
These plants alone provide Israel with nearly half its freshwater as 2015 and 70% by 2050.
IDE Technologies
Assuming an average American household consumes about 0.45 acre ft. per year, these plants could provide water to about 930,000 homes annually.

## Slide 10: Ashkelon Desalination Plant
4
The Ashkelon Plant is a well known desalination plant that uses reverse osmosis.
Its maximum output as of 2010 is roughly 120 million m3/year.
IDE Technologies

## Slide 11: Ashkelon Desalination Site
5
IDE Technologies
In fact, the company that developed many of these plants, such as the one in Ashkelon, is constructing the plant in Carlsbad, CA. The company is called IDE Technologies.

## Slide 12: Existing Desalination in CA
7
Carlsbad plant up and running by end of 2015
Catalina Island
Santa Barbara plant made during drought – never used due to higher cost than traditional methods.
Notes: Ocean water will be pumped to the desalination plant, where it will undergo a sand/anthracite fi ltration process to remove suspended particles from the water. Then, the water will be pumped through reverse-osmosis membranes that remove salts and other dissolved particles. Essential minerals will be added back into the water before it is piped to the Water Authority’s aqueduct as drinking water.
Both plants use reverse osmosis
http://www.sdcwa.org/sites/default/files/desal-carlsbad-fs-single.pdf
http://www.socalgreenrealestateblog.com/will-desalination-solve-californias-water-crisis/
http://www.santabarbaraca.gov/gov/depts/pw/resources/system/sources/desalination.asp
http://butier.com/projects/carlsbad-50-mgd-seawater-desalination-plant-and-product-water-pipeline/

## Slide 13: Large Scale Recycling

## Slide 14
10
Recycling Water
Involves purifying wastewater or sewage
Water can be used in utilities, irrigation, toilets, and in some cases for drinking and reservoir replenishment
Drinking water obviously must meet higher standards than basic grey water
Image Courtesy of Lenntech

## Slide 15
Once again, Israel is on the forefront of sustainability in terms of water.
As of 2010, they are able to recycle and essentially reuse 80% of their sewage as drinking water.
Recycling Water
The Jerusalem Post

## Slide 16
9
Pure Water San Diego

## Slide 17
8
Large Scale Recycling
Pure Water San Diego
In order to process large amounts of water in a clean manner, Pure Water and several other companies adopted this idea of Multi-Barrier Steps.
Each step, or barrier, of the purification process is a method of filtering out solid particles, bacteria, and other pollutants.
These steps may seem redundant, but they ensure that every drop of water meets the standards of safe irrigation and/or drinking respectively. (This also reassures the many people who feel doubtful about drinking water that came from sewage.)

## Slide 18: Clean Beyond Common Standard

## Slide 19: Policy Issues
Notes: Public Relations and Practices
Reasonable Use Laws
Water Supply Reliability

## Slide 20: Managing the Public: Triple Appeal Principle
The Id
The Ego
The Super Ego

## Slide 21: Managing Public Opinion
Water Recycling is Awe Inspiring for Some – Nauseating to Others

## Slide 22: Managing Residential Practices
Updates and Transparency Key for Public Cooperation

## Slide 23: Rewarding Practices
“California water servers and users have stepped up big time,” said Felicia Marcus, the chairwoman of the State Water Resources Control Board, as she announced the finding. “That is especially significant because June was really hot. The June numbers tell a story of conscious conservation.” – New York Times

## Slide 24: Small Scale Recycling

## Slide 25: Immediate and Long-Term Solutions
Chart: Short-Term Options
| Agricultural Water Use Efficiency | Precipitation Enhancement | Ground Water Storage | Urban Water Use Efficiency
 | 0.5 | 0.34 | 1.32 | 2.2
Chart: Long-Term Options
| Surface Storage (CALFED) | Conveyance | Ocean/Brackish Water Desalination | Recycled Municipal Water
 | 0.54 | 0.35 | 0.37 | 1.2
Median Cost Per Acre Ft
Source: California Coast Keeper Alliance 2009
$12000
10000
8000
6000
4000
2000

## Slide 26: Immediate Solution: Efficiency
Urban Water Use Efficiency
  California average reduction in June: 27%
  Next Goal: 32%
Benefits
  Reduce agricultural sacrifice
  Minimal resources to enforce

## Slide 27
15
Best Micro-Scale Water-Saving Techniques
Check faucets, pipes, and toilets for leaks can save from 20-200 gallons per day
Water-saving shower heads reduce waste up to 3 gallons per minute
Use Biodegradable soap so water can be easily used on plants
Low-flow faucet aerators

## Slide 28
13
Rainwater Capture Systems
Rainwater harvesting is the capture, diversion, and storage of non-potable water for later reuse.
-City of San Diego
Approximately 600 gallons of rainwater can be harvested from one inch of rain falling on a 1,000 square foot roof.

## Slide 29
14
Rainwater Capture Systems
Advantages
  Reduces demand on other sources such as ground and surface water
  Reduces water bill
  Water easily made suitable for irrigation
  Reduces floods and soil erosion
Disadvantages
  Unpredictable rainfall
  Initial cost from $200 to $2000
  Regular maintenance due to rodents, mosquitoes, algae growth, insects and lizards
  Roof types may seep chemicals or animal droppings
  Storage limits

## Slide 30
10
Long-Term Solution: Grey Water Recycling

## Slide 31
11
Advantages
  Reduce use of potable water to irrigate plants
  Reducing monthly water costs
  Minimize the burden on the public wastewater treatment system
  Complements drought tolerant and native landscapes
  Groundwater recharge
Disadvantages
  Health standards of the water and quality concerns
  Excessive filtration necessary to make water suitable for drinking
Greywater Recycling Systems

## Slide 32: Cost of Grey Water Systems
Chart: 
| System MSRP | Installation Fee | Yearly Maintenance
 | 6980 | 1560 | 236
High installation cost
Construction for individual buildings and homes are not cost effective.
Long construction and clean up
Data Source: The Guardian 2013

## Slide 33: Overcoming Grey Water Cost
Chart: NPV Over a 15 Year Operating Period
| Sharing (MBR) | Sharing (CW) | Individual Residential (CW) | Individual Office (CW) | Individual Residential (MBR) | Individual Office (MBR)
 | 332.4516 | 237.9156 | 158.9016 | -13.8372 | 183.5028 | -41.3088
Combined Systems
Larger capacity systems accommodate multiple buildings
Highest Water Savings potential
Divided cost between participants
Data Source: Sustainability 2013; doi:10.3390/su5072887

## Slide 34: Primary Regulation Updates
Redefine kitchen and dishwasher effluent as difficult to handle grey water.
Allow commercial and multi-family homes
Eliminate the mandate for a redundant irrigation system just for grey water distribution

## Slide 35
52
Better Practices for Energy Sustainability

## Slide 36: Brazilian PPT…….

## Slide 37: Contact us for more information
Phone: +1 619 595 0139
Address:
1088 3rd Ave
San Diego, CA 92101
Wrsc.org geni.org
@wrscnews @geninews
/WorldResourcesSimeCenter
/WRSCorg
Global Energy Network Institute - GENI
GIS Mapping Software
53

## Slide 38: Research Team
Ana Brandao
Arnaud Vedy
Ashjeet Talwar
Charlotte Muschamp
Chase Weinholtz
Clay Meyer
Derek Frommel
Daniel Garcia
Gabriela Simoes
Guilherme Barbosa
Leticia Carvalho
Pedro Matos
Renan Micha
Trevor Conger
55

## Slide 39: Questions
56